## Slide 1: Diagnostics Course
Unified Diagnostic Services

## Slide 2: Content
ISO 14229 Overview
Diagnostic Services & Sessions
Requests & Responses
Diagnostic and Communication Management Services
Stored Data Transmission
Data Transmission, InputOutput Control, Remote Activation
Upload Download

## Slide 3: Hexadecimal Format
Hexadecimal – base 16
  digits 0 to 9, A, B, C, D, E, F
  often denoted as $00, 00h, 00hex
dec | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
hex | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
dec | 16 | 17 | 18 |  | 32 |  | 48 |  | 255 | 256 | 257 |  | 65535
hex | 10 | 11 | 12 |  | 20 |  | 30 |  | FF | 100 | 101 |  | FFFF

## Slide 4: ISO 14229
Standard for Diagnostic Services
Mostly used over CAN, but can use any physical layer (network protocol)
De facto standard
Client (tester) and Server (ECU)

## Slide 5: ISO 14229
Client – the part (function) of an external tool or tester that makes use of the diagnostic services
Server – the part (function) of an ECU that provides diagnostic services
Client/Tester and Server/ECU often used interchangeably (but incorrectly)

## Slide 6: Application of ISO 14229
Ensure that an ISO 14229 tester can access the diagnostic services of an ISO 14229 ECU
  Scan Tools
  Manufacturing Tools (e.g. VCATS / eCATS)
  Engineering Tools (e.g. ASL / DVA / DHA)
  Test Tools
  Authorised Repairer Service Bay Tools (e.g. IDS)
Correct implementation of the diagnostic standard is essential to enable access for different tools

## Slide 7: What ISO 14229 Does Not Do
Determine network transmission format
Manage network communication
  flow control
  message arbitration
  error handling
Specify everything
find or fix the fault

## Slide 8: ISO 14229 Diagnostic Services
Definition: “An information exchange initiated by a client in order to acquire diagnostic information from a server and/or to modify its behaviour for diagnostic purposes.”
  25 diagnostic services
  many have subfunctions and parameters
  some mandatory, some optional
  positive and negative response

## Slide 9: ISO 14229 Diagnostic Services
hex | service name | subfunction / parameter
10 | DiagnosticSessionControl | diagnosticSessionType
11 | ECUReset | resetType
27 | SecurityAccess | securityAccessType securityAccessDataRecord
28 | CommunicationControl | controlType communicationType
3E | TesterPresent | zeroSubFunction
83 | AccessTimingParameter | timingParameterAccessType timingParameterRequestRecord
84 | SecuredDataTransmission | securityDataRequestRecord
85 | ControlDTCSetting | DTCSettingType DTCSettingControlOptionRecord
86 | ResponseOnEvent | eventType eventWindowTime eventTypeRecord serviceToRespondToRecord
87 | LinkControl | linkControlType baudrateIdentifier
Diagnostic and Communication Management Services

## Slide 10: ISO 14229 Diagnostic Services
hex | service name | subfunction / parameter
22 | ReadDataByIdentifier | dataIdentifier (list)
23 | ReadMemoryByAddress | addressAndLengthFormatIdentifier memoryAddress memorySize
24 | ReadScalingDataByIdentifier | dataIdentifier
2A | ReadDataByPeriodicIdentifier | transmissionMode periodicDataIdentifier (list)
2C | DynamicallyDefineDataIdentifier | defineByIdentifier dynamicallyDefinedDataIdentifier sourceDataIdentifier (list) positionInSourceDataRecord (list) memorySize (list)
2E | WriteDataByIdentifier | dataIdentifier dataRecord
3D | WriteMemoryByAddress | addressAndLengthFormatIdentifier memoryAddress memorySize dataRecord
Data Transmission

## Slide 11: ISO 14229 Diagnostic Services
hex | service name | subfunction / parameter
14 | ClearDiagnosticInformation | groupOfDTC
19 | ReadDTCInformation note that additional data may be included depending on the subfunction | reportNumberOfDTCByStatusMask reportDTCByStatusMask reportMirrorMemoryDTCByStatusMask reportNumberOfMirrorMemoryDTCByStatusMask reportNumberOfEmissionsRelatedOBDDTCByStatusMask reportEmissionsRelatedOBDDTCByStatusMask reportDTCSnapshotIdentification reportDTCSnapshotRecordByDTCNumber reportDTCSnapshotRecordByRecordNumber reportDTCExtendedDataRecordByDTCNumber reportMirrorMemoryDTCExtendedDataRecordByDTCNumber reportNumberOfDTCBySeverityMaskRecord reportDTCBySeverityMaskRecord reportSeverityInformationOfDTC reportSupportedDTC reportFirstTestFailedDTC reportFirstConfirmedDTC reportMostRecentTestFailedDTC reportMostRecentConfirmedDTC reportDTCFaultDetectionCounter reportDTCWithPermanentStatus
Stored Data Transmission

## Slide 12: ISO 14229 Diagnostic Services
hex | service name | subfunction / parameter
2F | InputOutputControlByIdentifier | dataIdentifier controlOptionRecord controlEnableMaskRecord
31 | RoutineControl | routineControlType routineIdentifier routineControlOptionRecord
InputOutput Control
Remote Activation

## Slide 13: ISO 14229 Diagnostic Services
hex | service name | subfunction / parameter
34 | RequestDownload | dataFormatIdentifier addressAndLengthFormatIdentifier memoryAddress memorySize
35 | RequestUpload | dataFormatIdentifier addressAndLengthFormatIdentifier memoryAddress memorySize
36 | TransferData | blockSequenceCounter transferRequestParameterRecord
37 | RequestTransferExit | transferRequestParameterRecord
Upload Download

## Slide 14: Diagnostic Sessions
All ECUs support one or more diagnostic sessions
  ECU is always in a diagnostic session
  ECU can only be in one diagnostic session at a time
  default diagnostic session on power-up, reset or timeout
A diagnostic session enables a set of diagnostic services and functionality
  set of services and functionality is ISO / OEM defined
  communication timing parameters can be changed when a new diagnostic session is entered
Not to be confused with security access levels
Notes: Diagnostic sessions are similar to the “modes” introduced by OBD-II.
JLR uses a generic specification (JLRDS, or Part 1) to define supported sessions, services and functions.

## Slide 15: Service Request
Service Identifier
Subfunction Identifier
Parameter(s)
XX
XXXXXXXX
XX
bit 7 reserved
XXXXXXXX
Source and Target Addresses
Notes: Addresses will not be considered here.

## Slide 16: Positive and Negative Response
ECU responds to service request
  positive response sent after execution of request
  exceptions for certain state-changing requests
  negative response sent if request cannot be executed
  response codes are defined

## Slide 17: Positive Response
The ECU sends a Positive Response if
  the message is received correctly
  the service and subfunction are supported
  the ECU is in the correct state for the request
  the response has not been suppressed
The Positive Response consists of
  the requested service identifier plus $40
  the subfunction requested and/or relevant parameters

## Slide 18: Positive Response Suppression
Positive Response can be suppressed for all services which support subfunctions
  bit 7 of subfunction byte = 1
  negative response is not affected
Notes: Why would you want to suppress the positive response?

## Slide 19: Negative Response
The ECU sends a Negative Response if
  the request message is invalid (e.g. too few parameters)
  it does not support the service or subfunction
  it is in an incorrect state for that request
  it cannot respond immediately
Prevents the tester waiting for a response
Physically addressed requests always result in a negative response if appropriate
Functionally addressed requests may result in a negative response if appropriate
  except for certain issues
Notes: Functionally addressed requests go to all ECUs, so a negative response is not sent for basic issues such as service/subfunction not supported. Too many responses would delay bus traffic.

## Slide 20: Negative Response
The Negative Response consists of
  the Negative Response identifier $7F
  the requested service identifier
  the Negative Response Code (NRC)
NRCs are defined in ISO 14229
  each service supports a particular set of NRCs

## Slide 21: Negative Response
Example NRCs
  $11 – Service Not Supported
  $12 – Subfunction Not Supported
  $13 – Incorrect Message Length or Invalid Format
  $22 – Conditions Not Correct
  $78 – Response Pending
Notes: NRCs are defined by ISO 14229. Technically, NRC refers only to this final descriptive byte, not to the entire negative response message.

## Slide 22: Response Pending NRC
Request received, but requested service is not yet complete and the ECU is not ready to receive another such request
  may be repeated by the ECU until the requested service is complete and the final response has been sent
  as soon as the requested service is complete, the ECU responds with a positive or negative response
  when a pending response is used the ECU always sends a final response even “suppress positive response” was used
  during Response Pending, the diagnostic session may need to be maintained using Tester Present

## Slide 23: Review
When is a Positive Response usually sent?
How many Diagnostic Sessions can an ECU support?
After the Service ID, what other data may be sent as part of a request?
When would a response not be sent?
Diagnostic Service Request and Responses

## Slide 24: Diagnostic Services
What does the service do?
How is it requested?
What responses are used?
What are the issues for this specific service?

## Slide 25: Diagnostic Services
The tester is in control
  requests always come from the tester
  the ECU can only respond to a request
The ECU does everything
  the tester does not clear DTCs
  the tester does not write data to memory
Notes: It is important to understand this. The tester and the ECU are completely separate entities, linked by a client-server relationship. Irrespective of the connection method, the tester cannot “do” anything to the ECU – it can only “request” the ECU to do something.
However, the tester remains in control of all operations. The ECU cannot autonomously request something from, or send something to, the ECU. (Periodic DID transmission is a special case but this remains under the overall control of the tester.)

## Slide 26: ISO 14229 Diagnostic Services
hex | service name
10 | DiagnosticSessionControl
11 | ECUReset
27 | SecurityAccess
28 | CommunicationControl
3E | TesterPresent
83 | AccessTimingParameter
84 | SecuredDataTransmission
85 | ControlDTCSetting
86 | ResponseOnEvent
87 | LinkControl
Diagnostic and Communication Management Services

## Slide 27: DiagnosticSessionControl
Default diagnostic session applies during normal ECU operation and when
  ECU is reset
  ECU does not receive TesterPresent and times out of another session
Other diagnostic sessions may be defined
This service requests the ECU to go into a specific diagnostic session
$10

## Slide 28: DiagnosticSessionControl
Some diagnostic sessions are defined
  $01 Default Diagnostic Session
  $02 Programming Diagnostic Session
  $03 Extended Diagnostic Session
  $04 Safety Diagnostic Session
Others are OEM specific
$10

## Slide 29: DiagnosticSessionControl
Byte | Description | Value
1 | DiagnosticSessionControl Request Service Id | 10
2 | diagnosticSessionType | XX
$10
Request
Notes: Which diagnostic session is being requested if byte 2 is 03?

## Slide 30: DiagnosticSessionControl
Byte | Description | Value
1 | DiagnosticSessionControl Request Service Id & $40 | 50
2 | diagnosticSessionType | XX
 | sessionParameterRecord | 
3 | P2can_server_max (MSB) | 00
4 | P2can_server_max (LSB) | 32
5 | P2*can_server_max (MSB) | 01
6 | P*2can_server_max (LSB) | F4
$10
Positive Response
Notes: Parameters for this service are the session timing parameters P2can_server_max (maximum time allowed for an ECU to respond to a service request, in this case 50ms) and P2*can_server_max (maximum time allowed for an ECU to respond to a service request after NRC $78 – Response Pending has been sent, in this case 5000ms).

## Slide 31: DiagnosticSessionControl
Byte | Description | Value
1 | Negative Response Identifier | 7F
2 | DiagnosticSessionControl Request Service Id | 10
3 | Negative Response Code | XX
$10
Negative Response

## Slide 32: DiagnosticSessionControl
Message | Tester | ECU
Request | 02 10 03 00 00 00 00 00 0 (single frame) 2 (2 bytes) 10 (Service ID) 03 (session type) | 
Positive Response |  | 06 50 03 00 32 01 F4 00 0 (single frame) 6 (6 bytes) 50 = 10 & 40 03 (session type) 00 32 01 F4 (parameters)
Negative Response |  | 03 7F 10 XX 00 00 00 00 0 (single frame) 3 (3 bytes) 7F (Negative Response ID) 10 (Service ID) XX (Negative Response Code)
$10
CAN Frames

## Slide 33: ECUReset
Performs a reset of the ECU
  reset type can be specified
Response sent before ECU restarts
ECU restarts in default diagnostic session
Most common type is “hard reset”
  implementation specific
  may re-initialize memory (volatile / non-volatile)
$11
Notes: ISO 14229 does not specify how the ECU reset process should be executed – this is OEM/supplier specific.

## Slide 34: ECUReset
Byte | Description | Value
1 | ECUReset Request Service Id | 11
2 | resetType | XX
$11
Request

## Slide 35: SecurityAccess
One or more “security access levels” may be defined for an ECU
  not to be confused with diagnostic sessions
  some services, DIDs and/or routines may require specific security access
Security protects against improper, unsafe, or damaging operation
This service requests the ECU to go into a specific access level
$27

## Slide 36: SecurityAccess
Based on seed-key mechanism
  tester requests the seed
  ECU sends the seed
  tester calculates the key using known algorithm
  tester sends the key
  ECU calculates the key and compares keys
  ECU responds
  ECU unlocks (if key is valid)
$27

## Slide 37: SecurityAccess
Only one security access level can be active at any time
Time delays and lock-outs may be used (ECU specific)
Security access is cleared when ECU is reset
If ECU is already at a security level and that level is requested again, zero seed is sent
$27

## Slide 38: SecurityAccess
Byte | Description | Value
1 | SecurityAccess Request Service Id | 27
2 | securityAccessType | XX
 | requestSeed (for level A) | 01
 | sendKey | 02
 | requestSeed (for level B) | 03
 | sendKey | 04
$27
Request
Notes: Security “levels” are arbitrary – the designation A, B etc is purely for clarification. The OEM can define up to 21 levels, each addressed by a pair of subfunction parameters (X, X+1).

## Slide 39: SecurityAccess
Byte | Description | Value
1 | SecurityAccess Request Service Id & $40 | 67
2 | securityAccessType | XX
 | if request was requestSeed | 
3-X | securitySeed (several bytes) | XXXX
$27
Positive Response

## Slide 40: SecurityAccess
Tester
ECU
$27
Request Seed
Send Key
Send Seed
Unlock & Send PR
Send NR
Send NR

## Slide 41: TesterPresent
“Keep-awake” message to ECU
Used to keep ECU in non-default diagnostic session
Transmitted periodically
$3E

## Slide 42: SecurityAccess
Byte | Description | Value
1 | TesterPresent Request Service Id | 3E
2 | zeroSubFunction | 00
$3E
Request
Notes: The “zero subfunction” is mandatory, but meaningless. ISO 14229 reserves other non-zero codes for possible future use.

## Slide 43: Other Services
Service | Description
CommunicationControl | The client requests the server to control its communication.
AccessTimingParameter | The client uses this service to read/modify the timing parameters for an active communication.
SecuredDataTransmission | The client uses this service to perform data transmission with an extended data link security.
ControlDTCSetting | The client controls the setting of DTCs in the server.
ResponseOnEvent | The client requests to start an event mechanism in the server.
LinkControl | The client requests control of the communication baud rate.

## Slide 44: Review
What two conditions may have to be met before gaining access to some data?
Why would an ECU switch from extended to default diagnostic session?
What does ECU Reset do?
Diagnostic and Communication Management Services

## Slide 45: ISO 14229 Diagnostic Services
hex | service name
14 | ClearDiagnosticInformation
19 | ReadDTCInformation
Stored Data Transmission

## Slide 46: ClearDiagnosticInformation
Requests the clearing (erasing) of DTCs and associated data from memory
  DTC, status byte
  snapshot and extended data
  other DTC-related information
Specifies single DTC, group of DTCs, or all DTCs
$14
Notes: Other DTC-related information could include the record of which was the earliest- or latest-recorded DTC, or any other flags, timers or counters not included in extended data.

## Slide 47: ClearDiagnosticInformation
Does not clear permanent DTCs
  MIL-requesting DTCs
  only cleared by OBD system in ECU
Does not operate on mirror / backup memory
  this relies on memory management strategy
ECU may need to be reset to fully clear memory
$14

## Slide 48: ClearDiagnosticInformation
Byte | Description | Value
1 | ClearDiagnosticInformation Request Service Id | 14
2-4 | groupOfDTC | XXXX
$14
Request
Notes: Group of DTC = 000000 for emissions-related DTCs, FFFFFF for all DTCs, otherwise OEM specific.

## Slide 49: ReadDTCInformation
Requests DTC and/or associated data from the ECU
  DTC, status byte
  snapshot and extended data
  other DTC-related information
Many subfunctions
$19

## Slide 50: ReadDTCInformation
Filtered or selected by
  Status Mask
  DTC Mask
  Snapshot Record Number
  Extended Data Record Number
  Severity Mask
$19
Notes: Filter by Status Mask: use the DTC Status Mask (see next page) e.g. to select all confirmed DTCs
Filter by DTC Mask: use the DTC code itself (to return data associated with that specific DTC)
Filter by Snapshot/Extended Record Number: different records may be maintained (e.g. snapshot on detected, on confirmed, etc)
Filter by Severity Mask: uses optional severity information for each DTC

## Slide 51: DTC Status (review)
Bit | Designation | Meaning
0 | testFailed | The test has reached its failure criteria (see next)
1 | testFailed ThisOperationCycle | Failure (0) occurred during this operation cycle
2 | pendingDTC | Latched when (0) occurs (i.e. stays set)
3 | confirmedDTC | As (2) for non-emissions-related faults Requires 2 or 3 operation cycles for emissions
4 | testNotCompleted SinceLastClear | Monitor test has not yet reached a pass/fail state since clear
5 | testFailed SinceLastClear | Failure (0) has occurred at least once since clear
6 | testNotCompleted ThisOperationCycle | As (4), but this operation cycle
7 | warningIndicator Requested | The fault requires that the MIL is illuminated

## Slide 52: DTC Status Mask
Notes: If any bit is set in both the status mask and the DTC Status Byte, the DTC is included.
Example: a status mask of $08 includes only those DTCs that have been confirmed.

## Slide 53: ReadDTCInformation
Byte | Description | Value
1 | ReadDTCInformation Request Service Id | 19
2 | reportNumberOfDTCByStatusMask reportDTCByStatusMask (also for mirror memory, emissions-related) | 01 02 XX
3 | DTCStatusMask | XX
$19
Request (DTCStatusMask)
Notes: DTCs can be reported from main (working) memory or from mirror memory, if used.
The search may be limited to emissions-related (OBD) DTCs.

## Slide 54: ReadDTCInformation
Byte | Description | Value
1 | ReadDTCInformation Request Service Id & $40 | 59
2 | reportNumberOfDTCByStatusMask | 01
3 | DTCStatusAvailabilityMask | XX
4 | DTCFormatIdentifier | XX
5-6 | DTCCount | XXXX
$19
Positive Response (DTCStatusMask)
Notes: Status Availability Mask defines which status bits are supported by the ECU (e.g. bit 7 – MIL Activation will probably not be supported by Body ECUs).
Format Identifier differentiates between four supported DTC formats including ISO 14229 and ISO 15031.

## Slide 55: ReadDTCInformation
Byte | Description | Value
1 | ReadDTCInformation Request Service Id & $40 | 59
2 | reportDTCByStatusMask | 02
3 | DTCStatusAvailabilityMask | XX
4-7 | DTCAndStatusRecord | XXXX
 | 4-7 may be repeated | 
$19
Positive Response (DTCStatusMask)
Notes: Status Availability Mask defines which status bits are supported by the ECU (e.g. bit 7 – MIL Activation will probably not be supported by Body ECUs).
DTC presented as high byte, middle byte, low byte (failure type), status byte.

## Slide 56: ReadDTCInformation
Byte | Description | Value
1 | ReadDTCInformation Request Service Id | 19
2 | reportDTCSnapshotRecordByDTCNumber reportDTCExtendedDataRecordByDTCNumber | 04 06
3-5 | DTCMaskRecord | XXXX
6 | DTCSnapshotRecordNumber DTCExtendedDataRecordNumber | XX
$19
Request (DTCMaskRecord)
Notes: DTC Mask Record sent as high byte, middle byte, low byte (failure type).
Record Number $FF returns all records.

## Slide 57: ReadDTCInformation
Byte | Description | Value
1 | ReadDTCInformation Request Service Id & $40 | 59
2 | reportDTCSnapshotRecordByDTCNumber reportDTCExtendedDataRecordByDTCNumber | 04 06
3-6 | DTCAndStatusRecord | XXXX
7 | DTCSnapshotRecordNumber | XX
8 | DTCSnapshotRecordNumberOfIdentifiers | XXXX
9-X | DTCSnapshotRecord | XXXX
 | 7-X may be repeated | 
$19
Positive Response (DTCMaskRecord)
Notes: Example shown is for Snapshot Data. Same format for Extended Data except “Number of Identifiers” is not included.

## Slide 58: Snapshot Data Example
DID | name | value | meaning
DD00 | Global Real Time | 0E 7A F5 4A | 281 days (approx)
DD01 | Odometer | 00 40 80 | 16 512km
DD02 | Battery Voltage | 39 | 14.25V
DD03 | Engine Status | 01 | Engine Running
DD04 | In Car Temperature | 37 | 15°C
DD06 | Power Mode | C3 | Post Accessory
$19
Notes: This is a real example from an L359 feedback file sent from a dealer.

## Slide 59: Extended Data Example
ID | name | value | meaning
01 | cycles since fault last detected | 7A | 122 cycles
02 | as above but where test was competed | 69 | 105 cycles
03 | cycles since fault first detected | 7A | 122 cycles
04 | total cycles in which fault was detected | 01 | 1 cycle
10 | fault detection counter | 80 | test passed
$19
Notes: This is a real example from an L359 feedback file sent from a dealer.

## Slide 60: ReadDTCInformation
Other subfunctions
  DTCs supported by the ECU
  First Test Failed DTC
  First Confirmed DTC
  Most Recent Test Failed DTC
  Most Recent Confirmed DTC
  “Prefailed” DTCs
  DTCs With Permanent Status
$19
Notes: Optional – may not be supported by the ECU.
Prefailed DTCs have a Fault Detection Counter from 1 to 126 ($01 to $7E) and are not pending or confirmed.

## Slide 61: Review
How could you find out how many confirmed DTCs were stored?
Do ECUs have to have mirror memory?
Does ClearDiagnosticInformation clear all DTCs and associated data?
Stored Data Transmission

## Slide 62: ISO 14229 Diagnostic Services
hex | service name
22 | ReadDataByIdentifier
2A | ReadDataByPeriodicIdentifier
2C | DynamicallyDefineDataIdentifier
24 | ReadScalingDataByIdentifier
2E | WriteDataByIdentifier
2F | InputOutputControlByIdentifier
23 | ReadMemoryByAddress
3D | WriteMemoryByAddress
31 | RoutineControl
Data Transmission, InputOutput Control, Remote Activation

## Slide 63: ReadDataByIdentifier
Requests the values of one or more DIDs
May require specific diagnostic session and/or security access (per DID)
Returned data is encoded (per DID)
  encoding (binary, ASCII, numeric etc)
  scaling & offset
  number of bytes
Encoding not sent with DID
$22
Notes: Although the Data Identifier code (the DID itself) must be two bytes, the DID value may be any number of bytes, encoded in any of several formats. This information is not provided by the ECU along with the DID value but must be separately requested by the ReadScalingDataByIdentifier service. Alternatively the encoding data must be “known” by the tester.

## Slide 64: ReadDataByIdentifier
Byte | Description | Value
1 | ReadDataByIdentifier Request Service Id | 22
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
 | 2, 3 may be repeated | 
$22
Request

## Slide 65: ReadDataByIdentifier
Byte | Description | Value
1 | ReadDataByIdentifier Request Service Id & $40 | 62
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
4-X | dataRecord | XXXX
 | 2-X may be repeated | 
$22
Positive Response

## Slide 66: ReadDataByPeriodicIdentifier
Periodic Data Identifiers are DIDs or DID combinations transmitted periodically
  specified by a single-byte code
  containing no more than six bytes of data
This service requests the transmission of one or more Periodic Data Identifiers
  data will be transmitted in successive Positive Response messages
  transmission will continue until stop requested
$2A
Notes: The single-byte code is the LSB of a two-byte DID (F2 00 to F2 FF).
The data length restriction allows the Periodic Data Identifier to be transmitted in a single CAN frame.

## Slide 67: ReadDataByPeriodicIdentifier
Byte | Description | Value
1 | ReadDataByPeriodicIdentifier Request Service Id | 2A
2 | transmissionMode | XX
3 | perioodicDataIdentifier | XX
 | 3 may be repeated | 
$2A
Request
Notes: Transmission Mode is slow, medium, fast, or stop.

## Slide 68: ReadDataByPeriodicIdentifier
Byte | Description | Value
1 | ReadPeriodicDataByIdentifier Request Service Id & $40 | 6A
$2A
Positive Response
Byte | Description | Value
1 | ReadPeriodicDataByIdentifier Request Service Id & $40 | 6A
2 | periodicDataIdentifier | XX
3-X | dataRecord | XXXX
Subsequent Periodic Response
Notes: Subsequent periodic response is sent separately for each Periodic Data Identifier.

## Slide 69: DynamicallyDefineDataIdentifier
Defines a set of DIDs and/or memory addresses for temporary use as a new DID
Dynamically defined DIDs can be read in the same way as permanent DIDs
Dynamically defined DIDs cannot be written
Dynamically defined DIDs can be cleared when no longer required
$2C
Notes: Dynamically defined DIDs can be cleared by explicit request, or they may be cleared during ECU reset or at other times (OEM specific).

## Slide 70: DynamicallyDefineDataIdentifier
Byte | Description | Value
1 | DynamicallyDefineIdentifier Request Service Id | 2C
2 | defineByIdentifier | 01
3, 4 | dynamicallyDefinedDataIdentifier | XXXX
5, 6 | sourceDataIdentifier | XXXX
7 | positionInSourceDataRecord | XX
8 | memorySize | XX
 | 5-8 may be repeated | 
 | 3-8 may be repeated | 
$2C
Request

## Slide 71: DynamicallyDefineDataIdentifier
Byte | Description | Value
1 | DynamicallyDefineIdentifier Request Service Id | 2C
2 | defineByMemoryAddress | 02
3, 4 | dynamicallyDefinedDataIdentifier | XXXX
5 | addressAndLengthFormatIdentifier | XX
6-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
 | 6-Y may be repeated | 
 | 3-Y may be repeated | 
$2C
Request

## Slide 72: DynamicallyDefineDataIdentifier
Byte | Description | Value
1 | DynamicallyDefineIdentifier Request Service Id | 2C
2 | clearDynamicallyDefinedDataIdentifier | 03
3, 4 | dynamicallyDefinedDataIdentifier | XXXX
 | 3-4 may be repeated | 
$2C
Request

## Slide 73: ReadScalingDataByIdentifier
Requests the scaling (encoding) data for a DID
Returned data is encoded (per DID)
  encoding (binary, ASCII, numeric etc)
  scaling & offset
  number of bytes
Encoding not sent with DID
$24

## Slide 74: ReadScalingDataByIdentifier
Byte | Description | Value
1 | ReadScalingDataByIdentifier Request Service Id | 24
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
$24
Request

## Slide 75: ReadScalingDataByIdentifier
Byte | Description | Value
1 | ReadScalingDataByIdentifier Request Service Id & $40 | 64
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
4 | scalingByte | XX
5-X | scalingByteExtension | XXXX
 | 5-X may be repeated | 
$24
Positive Response
Notes: Scaling Byte is composed of two elements: high nibble (0-F) represents data type, low nibble represents number of bytes. Multiple Scaling Bytes may be used if there are more than 15 bytes.
Scaling Byte Extension is mostly used for units though it has other specialized meanings.

## Slide 76: ReadScalingDataByIdentifier
$24
Positive Response Examples
24
F1 90
64
F1 90
6F
62
24
01 05
64
01 05
A0
30
24 – ReadScalingData
64 – ReadScalingData PR
F1 90 – VIN
01 05 – Vehicle Speed
6F – ASCII (15 bytes)
62 – ASCII (2 bytes)
A0 – Unit Format
30 – km/h
Notes: Scaling Byte is composed of two elements: high nibble (0-F) represents data type, low nibble represents number of bytes. Multiple Scaling Bytes may be used if there are more than 15 bytes.
Scaling Byte Extension is mostly used for units though it has other specialized meanings.

## Slide 77: WriteDataByIdentifier
Requests the writing of a DID value
May require specific diagnostic session and/or security access (per DID)
Typical uses
  programming configuration data
  resetting learned/selected values
  changing options (permanently or temporarily)
$2E

## Slide 78: WriteDataByIdentifier
Byte | Description | Value
1 | WriteDataByIdentifier Request Service Id | 2E
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
4-X | dataRecord | XXXX
$2E
Request

## Slide 79: WriteDataByIdentifier
Byte | Description | Value
1 | WriteDataByIdentifier Request Service Id & $40 | 6E
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
$2E
Positive Response

## Slide 80: InputOutputControlByIdentifier
Some DIDs may be “controlled” to simulate specific states
  input state, output state, internal state
Especially useful for driving outputs
May require specific diagnostic session and/or security access (per DID)
This service requests control access to one or more DIDs
$2F

## Slide 81: InputOutputControlByIdentifier
Byte | Description | Value
1 | InputOutputControlByIdentifier Request Service Id | 2F
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
4-X | controlOptionRecord | XXXX
X+1-Y | controlEnableMaskRecord | XXXX
 | 2-Y may be repeated | 
$2F
Request
Notes: Control Option Record may be: return control to ECU, reset to default, freeze current state, short term adjustment.

## Slide 82: InputOutputControlByIdentifier
Byte | Description | Value
1 | InputOutputControlByIdentifier Request Service Id & $40 | 6F
2 | dataIdentifier MSB | XX
3 | dataIdentifier LSB | XX
4-X | controlStatusRecord | XXXX
 | 2-X may be repeated | 
$2F
Positive Response

## Slide 83: ReadMemoryByAddress
Requests the data from a specified memory area
  specified by address and data length
May require specific diagnostic session and/or security access
$23

## Slide 84: ReadMemoryByAddress
Byte | Description | Value
1 | ReadMemoryByAddress Request Service Id | 23
2 | addressAndLengthFormatIdentifier | XX
3-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
$23
Request

## Slide 85: ReadMemoryByAddress
Byte | Description | Value
1 | ReadMemoryByAddress Request Service Id & $40 | 63
2-X | dataRecord | XXXX
$23
Positive Response

## Slide 86: WriteMemoryByAddress
Writes the data to one or more specified memory areas
  specified by address and data length
May require specific diagnostic session and/or security access
$3D

## Slide 87: WriteMemoryByAddress
Byte | Description | Value
1 | WriteMemoryByAddress Request Service Id | 3D
2 | addressAndLengthFormatIdentifier | XX
3-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
Y+1-Z | dataRecord | XXXX
 | 3-Z may be repeated | 
$3D
Request

## Slide 88: WriteMemoryByAddress
Byte | Description | Value
1 | WriteMemoryByAddress Request Service Id & $40 | 7D
2 | addressAndLengthFormatIdentifier | XX
3-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
$3D
Positive Response

## Slide 89: RoutineControl
ECU-based routines carry out specific actions
Often used instead of tester routines
May require specific diagnostic session and/or security access
This service requests a routine to start, stop, or return results
  some routines run until explicitly stopped
  some routines do not return data
$31

## Slide 90: RoutineControl
Byte | Description | Value
1 | RoutineControl Request Service Id | 31
2 | routineControlType | XX
3, 4 | routineIdentifier | XXXX
5-X | routineControlOptionRecord | XXXX
$31
Request
Notes: Routine Control Option Record includes any parameters required by the routine.

## Slide 91: RoutineControl
Byte | Description | Value
1 | RoutineControl Request Service Id & $40 | 71
2 | routineControlType | XX
3, 4 | routineIdentifier | XXXX
5-X | routineStatusRecord | XXXX
$31
Positive Response
Notes: Routine Status Record returns any data specified by the routine.

## Slide 92: RoutineControl
$31
Routine Example
31
02 01
71
02 01
31 – RoutineControl
71 – RoutineControl PR
01 – Start Routine
02 01 – Test Routine
01
01
Notes: This routine runs until stopped, while the technician wiggles a connector to determine if there are any intermittent open circuits.

## Slide 93: RoutineControl
$31
Routine Example
31 – RoutineControl
71 – RoutineControl PR
02 01 – Test Routine
31
02 01
71
02 01
02
02
02 – Stop Routine

## Slide 94: RoutineControl
$31
Routine Example
31 – RoutineControl
71 – RoutineControl PR
02 01 – Test Routine
XX XX XX XX – results
31
02 01
71
02 01
03
02
03 – Return Results
XX XX XX XX

## Slide 95: Review
what additional information might you need when reading a DID?
What do you need to know when writing data to memory?
How do you get data back from a routine?
Data Transmission, InputOutput Control, Remote Activation

## Slide 96: ISO 14229 Diagnostic Services
hex | service name
34 | RequestDownload
35 | RequestUpload
36 | TransferData
37 | RequestTransferExit
Upload Download

## Slide 97: Upload Download Overview
Three-stage handshake process
Initiate – Transfer – Terminate

## Slide 98: RequestDownload
Requests the initiation of a data transfer
Data is transferred from the tester to the ECU
ECU must confirm readiness with positive response
$34

## Slide 99: RequestDownload
Byte | Description | Value
1 | RequestDownload Request Service Id | 34
2 | dataFormatIdentifier | XX
3 | addressAndLengthFormatIdentifier | XX
4-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
 | 4-Y may be repeated | 
$34
Request
Notes: Data Format Identifier defines compression and encryption.
Address and Length Format Identifier defines number of bytes for Memory Address and Memory Size parameters.

## Slide 100: RequestDownload
Byte | Description | Value
1 | RoutineControl Request Service Id & $40 | 74
2 | lengthFormatIdentifier | XX
3, 4 | maxNumberOfBlockLength | XXXX
$34
Positive Response
Notes: Length Format Identifier defines number of bytes for Block Length parameter.
Block Length parameter defines maximum number of bytes in a TransferData block.

## Slide 101: RequestUpload
Requests the initiation of a data transfer
Data is transferred from the ECU to the tester
ECU must confirm readiness with positive response
$35

## Slide 102: RequestUpload
Byte | Description | Value
1 | RequestDownload Request Service Id | 35
2 | dataFormatIdentifier | XX
3 | addressAndLengthFormatIdentifier | XX
4-X | memoryAddress | XXXX
X+1-Y | memorySize | XXXX
 | 4-Y may be repeated | 
$35
Request
Notes: Data Format Identifier defines compression and encryption.
Address and Length Format Identifier defines number of bytes for Memory Address and Memory Size parameters.

## Slide 103: RequestUpload
Byte | Description | Value
1 | RoutineControl Request Service Id & $40 | 75
2 | lengthFormatIdentifier | XX
3, 4 | maxNumberOfBlockLength | XXXX
$35
Positive Response
Notes: Length Format Identifier defines number of bytes for Block Length parameter.
Block Length parameter defines maximum number of bytes in a TransferData block.

## Slide 104: TransferData
Requests the transfer of a block of data
Control of transfer is always by tester
Uses “block counter” to keep track of transfer
$36

## Slide 105: TransferData
Byte | Description | Value
1 | TransferData Request Service Id | 36
2 | blockSequenceCounter | XX
3-X | transferRequestParameterRecord | XXXX
$36
Request
Notes: For a download, the Transfer Response Parameter Record includes the data block to be transferred. For an upload, this record may include data parameters according to the OEM.

## Slide 106: TransferData
Byte | Description | Value
1 | TransferData Request Service Id & $40 | 76
2 | blockSequenceCounter | XX
3-X | transferResponseParameterRecord | XXXX
$36
Positive Response
Notes: For an upload, the Transfer Response Parameter Record includes the data block to be transferred. For a download, this record may include a checksum of the data received, or other such parameters, according to the OEM.

## Slide 107: RequestTransferExit
Requests the termination of a data transfer operation
$37

## Slide 108: RequestTransferExit
Byte | Description | Value
1 | RequestTransferExit Request Service Id | 37
2-X | transferRequestParameterRecord | XXXX
$37
Request
Notes: The Transfer Request Parameter Record is OEM specific.

## Slide 109: RequestTransferExit
Byte | Description | Value
1 | RequestTransferExit Request Service Id & $40 | 77
2-X | transferResponseParameterRecord | XXXX
$37
Positive Response
Notes: The Transfer Response Parameter Record is OEM specific.

## Slide 110: Review
How would you describe the Upload Download process?
Does ISO 14229 define a method for verifying the data?
When would you use Upload Download instead of Read Write by Memory Address?
For an upload, when would the transferred data be written to memory?
Upload Download

## Slide 111: ISO 14229 Diagnostic Services
No one service is more important than the others
  Services are used together to provide diagnostic functionality
Not all services are used, but the main problems arise when a service is not implemented correctly
  Some diagnostics could be improved by using more services
  Added diagnostic functionality
Notes: Which service is most important?

## Slide 112: Summary
ISO 14229 Overview
Diagnostic Services & Sessions
Requests & Responses
Diagnostic and Communication Management Services
Stored Data Transmission
Data Transmission, InputOutput Control, Remote Activation
Upload Download

## Slide 113: Feedback – Can the session be improved?
Your feedback is very important. Please spend a couple of minutes to share your thoughts about the lesson by completing your feedback form:
  Content – Was the content too deep, ok or too shallow?
  Pace – Was the pace too fast, ok or, too slow?
  Presentation – Was the presentation poor, ok or, good?
  Notes – Were the hand-outs poor, ok or good?
  Does the session need to be expanded or reduced? Leave blank if you think it is fine
Please include any additional comments you feel would help us to improve the quality of this lesson

## Slide 114: Questions